Sean Moloney
Professor Rivoire
CS 351: Computer Architecture
20 February 2017
Homework 1
Problem 1:
A) GPUs have been rapidly increasing in processing power. They are increasing at a faster rate than conventional CPUs. GPUs outperfome CPUs in floating point operations and also require less power to do so. Adding more cores would improve both the latency and throughput because they are simple chips.
B) This tells us the GPU is best used for very large computations.
C) How will the improvement on GPUs help use increase of knowledge of machine learning?
Problem 2:
A) One feature of ARM/LEGv8 to RISC ISA is its fixed width instruction set.
B) CPU1 = 1.7 * .6 GHz = 1.02
CPU2 = 1.5 * 1.66 GHz = 2.44
CPU1 is 2.44 times slower than CPU2
C) {1} over {1-.37 {.37} over {2} } = {1} over {.63 {.37} over {2} } = {1} over {.815} = 1.227
The improved bwaves would have a 1.227 speedup over the old bwaves.
D) The ARMv8 processor will perform th benchmark faster than the i7.

Problem 3:
A)
Known:
It will take 100 seconds on 1 core
up to 50 seconds of this can be parallelized with a perfect linear sped up
Splitting it onto two cores will reduce it by 25 seconds
For 2 cores:
100 seconds – 25 seconds = 75 seconds.
We then need to adjust this time for the difference in clock speed 75 seconds - {3.06GHz} over {3.20Ghz} approx 71.72 seconds

For 4 cores:
Since we know that it will take 25 seconds when it is split onto two cores, we must divide this number again by two when we split it onto four cores.
{25 seconds} over {2} = 12.5 seconds Then we add it to the 50 seconds for it to be parallelized.
50 seconds + 12.5 seconds = 62.5 seconds
Finally, we must adjust for the clock speed
62.5 seconds x {2.26hz} over {3.20GHz} approx 44.14 seconds

B)